SECTION 05 73 13

GLAZED DECORATIVE METAL RAILINGS

VENTUS™ GLASS + METAL CRAFT WINDSCREEN SYSTEM

PART 1	GENERAL

1.1	SECTION INCLUDES

- Fabricated Glazing.

- Structural Posts and Fittings.

- Attachment to Structure.

1.2	RELATED SECTIONS

- Section 05 52 00 - Metal Railings.

- Section 05 73 00 - Decorative Metal Railings.

- Section 08 80 00 - Glazing.

1.3	REFERENCES

- ANSI Z97.1 - Safety Glazing Material Used in Buildings.

- ASTM E 985 – Standard Specification for Permanent Metal Railing Systems and Rails for Buildings.

- ASTM C1048 - Standard Specification for Heat Treated Flat Glass, Coated and Uncoated Glass.

1.4	DESIGN REQUIREMENTS

- Windscreen system shall be designed to conform to building code and ADA requirements for openings and stress.

- Performance Requirements for Windscreen Assembly:

  - Support distributed load of 50 pounds per linear foot (8,756 N/M), applied horizontally at right angles to the handrail.

  - Support concentrated horizontal load of 200 pounds (90.6 kg), applied in any direction at any point along handrail system.

  - Distributed loads and concentrated loads not to be applied simultaneously.

  - Wind Load: Windscreens must be capable of withstanding the project specific wind loads without exceeding allowable design working stress of materials for handrails, railings, anchors, and connections.

1.5	SUBMITTALS

- Submit under provisions of Section 01300.

- Shop Drawings:  Submit Shop Drawings for windscreens.

  - Include plans, elevations, and details.

  - Include design loads, structural calculations, and material properties.

  - Provide Shop Drawings signed and sealed by structural engineer licensed in the state in which Project is located.

- Submit manufacturer's samples of finishes.

- Maintenance Instructions:  Submit manufacturer's maintenance and cleaning instructions.

- Warranty:  Submit manufacturer's standard warranty.

1.6	DELIVERY, STORAGE, AND HANDLING

- Deliver materials properly protected against damage to finished surfaces during transit.

- Inspect materials upon delivery for damage. Unless minor defects can be made to meet the Architect’s specifications and satisfaction, damaged parts should be removed and replaced.

- Store materials at building site under cover in dry location

PART 2	PRODUCTS

2.1	MANUFACTURER

- Basis of design; “VENTUS” glass and metal windscreen system by Glass & Metal Craft; www.glassandmetalcraft.com

- Substitutions: Not Permitted.

2.2	MATERIALS

- Stainless Steel Components: Conforming to ASTM A 666

  - Type 316 (exterior)

2.3	 COMPONENTS

- Tempered Laminated Glass: 2-Ply tempered glass laminated in accordance with ASTM C1172.

  - Laminated Safety Glass: Complies with ANSI Z97.1 and 16 CFR1201 test requirements for Category II.

  - Thickness: 13/16” Minimum Laminated Glass.

  - Color: Clear, or tint. (Architect to specify.)

  - SentryGlas Ionoplast Interlayer: 0.060 inch thick, minimum, clear.

- Posts:

  - Material: Stainless Steel or Powder Coated Steel

  - Shape: Tapered plate

  - Mounting Method: Surface Mounted

- Anchors: Select fasteners of type, grade and class required to produce connections suitable for anchoring system to other types of construction indicated.

  - For concrete attachment.

  - For steel attachment

2.4 	FABRICATION

- Fabricate windscreen assembly components to lengths and configurations complying with shop drawings.

- Machine joint edges smooth and plane to produce hairline seams when site assembled; supply concealed sleeve connectors for joints.

- Isolate dissimilar metals to prevent electrolytic action by applying primer to concealed surfaces of metal components.

PART 3	EXECUTION

3.1	INSTALLATION

- Install windscreens in accordance with manufacturer’s recommended installation instructions and approved shop drawings.

3.2	CLEANING

- Clean glazing surfaces after installation, complying with requirements contained in the manufacturer’s instructions. Remove excess glazing sealant compounds, dirt or other substances.

- Remove protective films from metal surfaces.

- Clean railing surfaces with clean water and mild detergent. Do not use abrasive chemicals, detergents, or other implements that may mar or gouge the material.

3.3	PROTECTION

- Institute protective measures required throughout the remainder of the construction period to ensure that all the materials do not incur any damage or deterioration.

- Repair components damaged by subsequent construction activities in accordance with manufacturer’s recommendations; replace damaged components that cannot be repaired to Architect’s acceptance.

END OF SECTION